Introduction

The goal of this project is the implementation of a “digital picture box” that acts as an interface between a PC and any VGA compatible device for the display of JPEG images. Display options and image selection are implemented with the use of on-device push buttons (next, previous, function and power) as well as an IR remote control. Device status is indicated with the use of power and busy LED’s. The physical interfaces are between an RJ-45 port and a 15 pin female VGA connector.

Reliability issues pertinent to this project include component error, durability, emissions (heat and noise), speed and accuracy of image processing and image display. Safety issues were taken into account by securely casing the internal electronics and should not be a factor during normal operation. The aim of analyzing reliability and safety issues is to achieve the best performance with minimal cost and maximum customer satisfaction. This is an important aspect of any products development process as it investigates any possible dangers or unwanted effects that may be experienced by the end user.

With this in mind this document contains a reliability analysis of 5 major design components that are most likely to fail, or are critical to design operation, with calculations of failure rates for each component. In addition an FMECA (failure, mode, effects, and criticality analysis) worksheet for the entire schematic grouped into functional blocks is attached. Lastly a reference list of component data sheets and sources for calculation, analysis variables and equations is included.

Reliability Analysis

The 5 design components with the highest probability of failure due to heavy use during operation are (i) Low Drop Out Voltage Regulators: 9V – 3.3V analog and digital and 9V – 5V digital, (ii) Rabbit 3000 microprocessor, (iii) IR receiver/decoder, (iv) EPSON graphics controller, (v) DRAM memory chip.

Analysis and calculations are done with reference to the formulas and variables in the Military Handbook Reliability Prediction of Electronic Equipment [2].

Failure rate calculation variables :

MTTF: Mean time to failure (λp)-1

λp  : represents the predicted number of failures per 106 hours of operation.

λBD : die base failure rate

λBP : package base failure rate

λEOS : electrical overstress failure rate

λcyc : cycling factor

C1 : die complexity constant

C2: pin number constant

πT : temperature coefficient, based on junction temperature

πE : environmental constant, based on equipment use environment

πQ : quality factor, military (1-2) or commercial 3 -10

πL : learning factor, based on years device type has been in production

πMFG : manufacturing process correction factor

πCD : die complexity correction factor

πPT : package type correction factor

(i)   LDO Voltage Regulator : 9V – 3.3V analog ( Texas Instruments REG103-33 )

Linear MOS Device    λp = (C1πT + C2πE )πQ πL

| Parameter | Value | Justification |
| --- | --- | --- |
| C1 | 0.02 | Linear, 101 – 300 transistors |
| πT | 7.0 | Linear, MOS, TJ < 85 0 C (assuming max temp.) |
| C2 | 0.0025 | SMT, 6 functional pins, non hermetic |
| πE | 2.0 | Ground fixed environment |
| πQ | 10 | Commercial |
| πL | 1.0 | Years in production > 2.0 |

Table 1.

λp = (0.02*7.0 + 0.0025*2.0)10*1.0 = 1.45/106 hours

MTTF = 1/ λp = 689 655.17 hours = 78.73 years

The 9V-3.3V digital and 9V-5V digital are all in the same LDO regulator family of components from the same manufacturer and so the above calculations are applicable in determining failure rates for those components.

(ii)  Rabbit 3000 microprocessor

Digital MOS Microprocessor  with > 60000gates  λp = λBDπMFGπTπCD + λBPπEπQπPT + λEOS

| Parameter | Value | Justification |
| --- | --- | --- |
| λBD | 0.16 | Logic device |
| πMFG | 2.0 | Non QML or Non QPL |
| πT | 0.88 | Digital MOS, TJ < 85 0 C (assuming max temp.) |
| πCD | 25 | 1.6 cm2, assume 1 micron size |
| λBP | 0.0044 | 128 pins |
| πE | 2.0 | Ground fixed environment |
| πQ | 10 | Commercial |
| πPT | 6.1 | Non hermetic, surface mount |
| λEOS | .065 | Max voltage is 5.5v , ESD Susceptibility |

Table 2.

λp = 0.16*2.0*0.88*25 + 0.0044*2.0*10*6.1 + 0.065 = 7.6418/106 hours

MTTF = 1/ λp = 130 859.22 hours = 14.938 years

The rabbit microprocessor is being used as part of the core module which includes additional components ( SRAM, Flash and Ethernet) which will affect the reliability and performance.

(iii) 14-bit IR Decoder (IR-D14 IC)

Digital Microcontroller    λp = (C1πT + C2πE )πQ πL

| Parameter | Value | Justification |
| --- | --- | --- |
| C1 | 0.02 | MOS Digital, assume < 1000 gates |
| πT | 0.88 | MOS Digital , TJ < 85 0 C (assume same max temp) |
| C2 | 0.0034 | SMT, 8 functional pins, non hermetic |
| πE | 2.0 | Ground fixed environment |
| πQ | 10 | Commercial |
| πL | 1.0 | Years in production > 2.0 |

Table 3.

λp = (0.02*0.88 + 0.0034*2.0)10*1.0 = 0.244/106 hours

MTTF = 1/ λp = 4 098 360.65 hours = 467.84 years

(iv) EPSON Graphics Controller (S1D13505 )

LCD/CRT Controller   λp = (C1πT + C2πE )πQ πL

| Parameter | Value | Justification |
| --- | --- | --- |
| C1 | 0.08 | MOS Digital, assume 30,001 to 60000 gates |
| πT | 0.88 | MOS Digital , TJ = 85 0 C (max operating temperature) |
| C2 | 0.068 | SMT, 128 functional pins, Non hermetic |
| πE | 2.0 | Ground fixed environment |
| πQ | 10 | Commercial |
| πL | 1.0 | Years in production > 2.0 |

Table 4.

λp = (0.08*0.88 + 0.068*2.0)10*1.0 = 2.064/106 hours

MTTF = 1/ λp = 484 496.12 hours = 55.31 years

(v) 16-Bit EDO DRAM chip.

MOS Memory Device    λp  = (C1πT + C2πE + λcyc )πQ πL

| Parameter | Value | Justification |
| --- | --- | --- |
| C1 | 0.01 | DRAM, Memory size > 256K |
| πT | 5.0 | Memories , TJ < 85 0 C ( max operating temperature) |
| C2 | 0.019 | SMT, 40 functional pins, Non hermetic |
| πE | 2.0 | Ground fixed environment |
| λcyc | 0 | Non EEPROM device |
| πQ | 10 | Commercial |
| πL | 1.0 | Years in production > 2.0 |

Table 5.

λp = (0.01*5.0 + 0.019*2.0 + 0)10*1.0 = 0.88/106 hours

MTTF = 1/ λp = 1 136 363.63 hours = 129.72 years

Summary and Conclusions

| Component | Description | λp / 106 hours | MTTF years |
| --- | --- | --- | --- |
| U14 | LDO voltage regulator (REG103-33) | 1.45 | 78.73 |
| R1* | Rabbit 3000 Microprocessor | 7.64 | 14.94 |
| U16 | IR Decoder | 0.24 | 467.84 |
| U10 | EPSON Graphics Controller | 2.06 | 55.31 |
| U9 | EDO-DRAM | 0.88 | 129.72 |

Table 6. Component failure rate summary         ( R1* Only rabbit headers are on schematic )

From the above table it can be seen that among the 5 components analyzed, the Rabbit Microprocessor is the most likely to fail by a large margin. Given that all calculations were made using a maximum operating temperature of 850 C as compared to the standard 250 C these error rates are higher than what would occur during normal operation of the circuit. It is still valuable however to reduce error rates as much as possible and this could be achieved by adding a heat sink to both the Rabbit and the EPSON extending the theoretical lifetime of the digital picture box.

FMECA (Failure, Mode, Effects and Criticality Analysis)

In conducting the FMEC Analysis, the DPB schematic is divided into its major functional blocks:

| Blocks | Category | Components |
| --- | --- | --- |
| A | Power Supply | 9V Wall wart, Voltage regulators |
| B | User Interface | Push buttons, IR Decoder and Receiver |
| C | Physical connectors | VGA Connector, RJ-45 (on core module) |
| D | Graphics | EPSON, DRAM, PLDs , Crystal Oscillator |
| E | Microcontroller | Rabbit 3000, Reset controller |

See attached worksheet for detailed analysis of  all possible failure conditions for each block, the resulting effects on other parts of the design and the level of criticality for each type of failure.

There are two basic levels of criticality as pertains to this project:

LOW - meaning the overall output of the design will not be impacted and a display is still visible on the display device.

HIGH - meaning the output will be affected and the design not function as expected. Specifically a distorted image or no image at all present on the display device. For LOW criticality failures a rate of λ < 10-4 will be accepted and for HIGH criticality failures a rate of λ < 10-9 errors per hour of operation.

References

[1] “Designing for Reliability, Maintainability and Safety – Parts 1,2 and

3”, Circuit Cellar, December 2000, January 2001, April 2001.

[2] MIL-HDBK-217F Reliability Prediction of Electronic Equipment

http://shay.ecn.purdue.edu/~dsml/ece477/Homework/Spring2004/Mil-Hdbk-217F.pdf

[3]  Low-Drop Out Voltage Regulators

3.3 V : http://focus.ti.com/lit/ds/symlink.reg103-33.pdf

5 V: http://focus.ti.com/lit/ds/symlink.reg103-5.pdf

[4]  Rabbit 3000 Core Module

http://www.rabbitsemiconductor.com/products/rcm3000/index.shtml

[5] IR Decoder

http://shay.ecn.purdue.edu/~477grp12/datasheets/rentron_ir_decoder.pdf

[6] EPSON Graphics Controller

http://shay.ecn.purdue.edu/~477grp12/datasheets/epson_manual.pdf

[7] EDO-DRAM

http://www.issi.com/pdf/41xx16256.pdf

[8] Crystal Oscillator

http://www.eea.epson.com/go/Prod_Admin.Categories/EEA/QD/Crystal_Oscillators/all_oscillators/go/resources/TestC2/SG8002DB

Appendix H: FMECA Worksheet

| Failure No. | Failure Mode | Possible Causes | Failure Effects | Method of Detection | Criticality | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
| Block A: Power Supply |
| A1 | Vcc = 0V | Failure of J6 or failure of U13, U14, U15 ( Any component in Block A fails or an external short) | No power to U10, therefore no image displayed at all. | Observation | HIGH |  |
| A2 | Vcc > 5V | Failure of U13, U14, U15 | Unpredictable effects | Observation | HIGH |  |
| A3 | Vcc out of tolerance | C7, C20, C8 | High ripple or Operation at out of spec voltage; Unpredictable | Observation | HIGH | Monitor Wall Wart |
| Block B: User Interface |
| B1 | No response to pushbuttons | SW2, SW3, SW4, SW5 | No new pictures obtained | Observation | LOW | Limits the users control method to IR remote |
| B2 | IR fluctuating or corrupted | U16, U17 | Random pictures displayed for undetermined periods of time | Observation | HIGH |  |
| Failure No. | Failure Mode | Possible Causes | Failure Effects | Method of Detection | Criticality | Remarks |
| Block B: User Interface |
| B3 | One of IR decoder outputs (PE0 - 4) stuck at 1. | U16,U17 | Infinite cycle through images; Switching on and off continuously | Observation | HIGH |  |
| Block C : Physical Connectors |
| C1 | All Outputs 0 | U10, J8 R39,R40,R41, D5,D6,D7 | No pixel data sent out on VGA connector | Observation | HIGH | Replace connector |
| C2 | All Outputs 1 | U10, J8 R39,R40,R41, D5,D6,D7 | Wrong data on output connector; Unpredictable effects | Observation | HIGH |  |
| C3 | Random Outputs | U10, J8 R39,R40,R41, D5,D6,D7 | Unpredictable effects | Observation | HIGH |  |
| Block D: Graphics |
| D1 | Incorrect PLD outputs | U2, U3, U7 | Pixel data sent to the wrong addresses, corrupted display | Observation | HIGH |  |
| D2 | PLDs Outputs all 0 | U2, U3, U7, J5, U13 | No addressing information available | Observation | HIGH | Bad Chip |
| D3 | PLDs Outputs all 1 | U2, U3, U7 | Same Address is sent pixel data and is overwritten each time | Observation | LOW |  |
| Failure No. | Failure Mode | Possible Causes | Failure Effects | Method of Detection | Criticality | Remarks |
| D4 | EPSON all Outputs 0 | U10, Q1, J20,U13 | No meaningful data buffered in DRAM or sent to VGA output; Unpredictable | Observation | HIGH | User gets incorrect data from PC. Product is not useful. Easily detected. |
| D5 | EPSON all Outputs 1 | U10, Q1, J20,U13, C1 – C6, C11 – 13 | No meaningful data buffered in DRAM or sent to VGA output; Unpredictable | Observation | HIGH |  |
| D6 | Clk always high (1) | U12 | EPSON’s communication and synchronization with rest of circuit is affected; can’t interface easily | Observation | HIGH |  |
| Block E : Microcontroller |
| E1 | All outputs 0 | Failure in μC , U15, J6 | NO functionality, interfacing, image transferring, No output at all | Observation | HIGH | Use reset controller |
| E2 | All Outputs 1 | Failure in μC | Unpredictable | Observation | HIGH | Reset μC |
| E3 | Random outputs | S/W problem | Unpredictable effects | Observation | HIGH | Use headers to test S/W |